# PA3BJI
# ir. F.H.(Frans) Evenblij
# February 2016
# NBFM 23cm Architecture and Design
# For the PE1JPD 23-cm narrow band FM transceiver

# Preface
# This document describes alternative firmware for the 23 CM Narrow Band FM transceiver designed by Bas PE1JPD.
# Software Architecture
# Views:
# Use-case view Describes particular relevant use-cases and use-cases with a high architectural imapact.
# Logical view Describes decomposition in moduls, layers, packages and relations.
# Process view Describes the way classes, modules and subsystems are modeled on to processes and threads.
# Deployment view Describes the distribution of software artefacts over system nodes.
# Implementation view
# Data view Describes the system from the point of data storage and retention.
# Integration view Describes the system in terms of its relation to related systems
  1. Menu-system
# Normal control of the transceiver takes place via dedicated switches on the front-panel, combined with a multi-purpose rotary-dial and a menu-system.
Figure 1. Simplified Menu structure

Start/
Select

Menu/
back

level
tone

shift
PTT

Shift
main-loop

(slow)
Display

  1. Data-flow
Data and control flow takes place according to the diagram below. This diagram describes the software in its interaction with the hardware level.

Tranceiver
State
Description
Outputs :
* Display
* Mute
* PLL

Inputs :
* Rotary Dial
* S-meter ADC
* PTT,
* etc...

Remote Control
via UART
USB Outputs:
Audio
Status data

Non-volatile
memory

RS232
Wifi / Bluetooth

Event-Timer
Figure 2. Data flow of the software .
Transceiver state can be changed both by input controls, and by remote control commands. Remote commands are entered into the system by any of the implemented remote control channels. This will be a serial line equivalent, either over real RS232, or as a serial channel via USB, Wifi or BlueTooth.
  1. IO system
Inputs controls
These are the controls present on the front-panel of the tranceiver. They are supported by tranceiver hardware
1. Rotary dial
2. Selector push button
3. Shift enable toggle switch
4. Tx/Rx toggle switch
5. S-meter ADC (internal signal, not on front-panel)

Each of the controls above are supported by the hardware. There are however more function that we'd like to implement and the need some kind of control. Until a hardware redesign has been made with support for extra input controls, the extra functions can be controled via a remote-control interface.
In order to avoid discrepancy between the remote-control signals and the front-panel controls, we need to be carefull with the way a control handler is implemented.

Rotary dial.
The rotary dial provides a relative control, so there is no potential conflict between the rotary dial en remotely entered data.
Selector push button
This function control the menu system. The menu is not needed for remotly entered data, so no discrepancy is possible.
Shift enable toggle switch
On the front panel this is a toggle switch with an absolute value indication. Up is shifted, down is not shifted. Here we have a potential clash between the position of the switch and the setting provided by the remote-control interface. For the moment we will solve this problem by looking only at the position changes in the software, and communicate the enable and disable commands to the processing stage of the software. An enable command by the toggle switch can be overriden by the remote-control facility, but by using a marker no the LCD display, the user can be kept in formed on the state of the shift function.
Tx/Rx toggle switch
Here we have the same issue as with the shift enable toggle switch. Again, we'll solve this by communicating the state changes to the processing software and informing the user via the display.
S-Meter ADC
This is an internally generated signal. It will be presented on the LCD display, and the S-Meter value will be communicated to the remote-control position. No discrepancy between front-panel and remote-control panel is possible.
Output Controls
1. PLL synthesizer controls (programming of the PLL synthesizer chip)
2. Display controls (presentation on LCD display)
3. CTCSS signal (injection of signal frequency during transmit)
4. Audio mute switch (switch off the audio path)
5. S-meter display (discrete indication on LCD display)
  1. Memory system
    1. Volatile transceiver state
input related
- rotary dial, up/down action
- selector switch
- repeater shift enable
- tr/rx (ptt)
internal
- menu position
- ctcss tone value
- S meter mute value
- base frequency
- VFO Tx/Rx shift value
- repeater shift value
- scanning
- main-menu state
- sub-menu state
- direct menu return
output related
- display frequency
- display s-meter
- display T/R
- display M
- display menu
- current PLL frequency
- muted yes./no
- transmitter on
    1. Non volatile memory
- BaseFrequency
- Mute level
- Repeater Shift value
- CTCSS tone value
    1. Program flow
1. process input date to input-state variables
2. process input-state and process-state to output-state
3. process output-state to output data
  1. Possible function extensions
For test and simulation:
- Create simulation of the display, PLL and tone outputs.
- Create simulation of the toggle, push button and rotary switches.
- Create drivers between keyboard, video display and I/O-simulation.
Software Improvements
- Store repeater shift with repeater frequency
- Store CTCSS frequency with repeater frequency
- Use automated shift whenever the repeater frequency is selected
- show programmed repeater call instead of frequency (or both in scroll mode)
- Priority Channel: Listened on every 2 seconds for activity and stays there when activity is detected.
- √ Scan between start and end frequency for empty or used channels
- √ Provide for 25kHz as well as selectable step size during tuning
Advanced functions
- Set/Change PLL reference frequency (for example to change the 12Mhz XTO to a 13 MHZ TCXO)
- Run a PLL channel jump function to generate a square wave on the VCO control line. Allow for multiple step times and frequency settings. Use full for performing measurements on the Phase Locked Loop.
When extra switches front panel switches are present
- Provide 16 or 32 preferred channels. Change from “free dial” to “choose channel” functionality by a setting in the configuration menu.
- Start/Stop scan button
- Reverse shift toggle switch
Hardware improvements
- √ Get rid of 650 MHz spurious output (not in my version)
- Increase stability of reference timebase (use TCXO by PA0PYL)
- Add 900 MHz filter against GSM interference
- Add noise triggered squelch
- Add reverse shift push button
- Improve CTCSS filtering and injection
- Add TX output lowpass filter (3 pole)
- See if PLL loop filter needs optimization
Serious circuit changes
- Add additional input and output channels on the μController via port extension chips
- Add Bluetooth and/or WiFi interface for remote control
- Add USB interface for remote control
- Add analog meter as S-Meter
Remote control only commands
- Read system-state
- Write system-state
- All functions that require extra input hardware can be controlled via the remote control mechanism.
# Design
# The core of the system is the systems main-loop. This loop does three things:
# Collect inputs and stores them into the system-state memory.
# Performs processing of input related variables and transforms them to output related variables that are handled in the final part of the main loop.
# Inspect system-state memory and set output values or call output routines.
# Like the name implies, the content of the system-state memory thus determines the state of the system. Apart from the physical controls , the menu system will also have its impact on the content of the system state memory.
# The system is designed in such a way that is possible to modify the content of the system-state memory by remote control in order to implement remote control functionality.
# Basically, remote control is implemented by a command-line parser that takes its input from a chosen channel, and modifies the output related values of the system-state memory accordingly. The command-line can be handled via a UART function. At the hardware level the UART will be connected to one of several possible transmission channels:
# RS232 level converter for classic RS232.
# Bluetooth serial interface.
# WiFi serial interface.
# A web-server running on an Arduino, implementing a web-service that might be presented on the internet.
## Input functions
## The inputs described here are physical inputs available in the current version of the hardware design (version 2 ??)
## Some of the inputs are handled by interrupt driven software. Currently these are the rotary-dial, and the selector-push-button switch. Both of these are inputs where the number of signal changes are relevant to there function, while both inputs are by way of their mechanical switch, likely to suffer from mechanical contact bounce and potential erroneous behavior.
## The interrupt routine will take care of the necessary delays in the signal processing, without disturbing the working or the responsiveness of the rest of the system.
## The other input controls are handled in the main loop by simple signal sampling. Although these mechanical switches are not immune to contact bounce, the nature of the sampling process guarantees the there is no problem with bounce.
## The main loop calls the functions defined in this chapter and places their output values into the system-state memory.
## Rotary Dial
Interrupt driven part
## The rotary dial has two “pull down to ground” lines. The first line (A) is connected to an interrupt sensitive input. It should trigger on both positive and negative edges. If that is not in hardware available, than the edge sensitivity should be programmatically changed on every interrupt that occurs
## The Interrupt Service Routine (IRS) samples input (B) and starts the anti-bounce and direction-detect algorithm.
## The result of the anti-bounce and direction-detect algorithm is written to the internal system state area. From there it is picked up by the output processor.
Initialization
## During initialization after system power up, the rotary dial count Values will be set to 0 (zero)..
Main-loop driven part
## InputGetRotaryDialCount()
This function is called from the main loop, and its output is stored into the system-state memory.
## Outputs of the function are the following:
## Direction (up/down or left/right) indicator. Incremented for every step up or right, and decremented for every step down or left.
## Reading the output of the rotary dial is done by the routine GetRotaryDialCount().
## Before reading it will disable the A-line interrupt, read the content, set content to null, and re-enable the A-line interrupts.
## The Values returned will indicate how many steps of the rotary dial have been made and will have to be processed. A zero return Values means no actions needs to be taken.
Return Values R	Action
R < 0	Take R steps to the left or down.
R == 0	Take no action
R > 0	Take R steps to the right or up.
Table 1. Return values of GetRotaryDialCount()
## Selector push button
## Interrupt driven part
## The selector push button contains a pull-down-to-earth switch, Interrupts will be generated on the falling flank of the signal. Before starting the processing within the ISR, a time will be checked to verify that an earlier interrupt is at least 10 milliseconds into the past. If an interrupt occurred earlier, it is assumed that the current interrupt is cause by contact bounce, and ignored. The timer will be reset to 0 ms and a return from interrupt instruction will be executed at once.
Initialization
## During initialization after system power up, the timer Values will be set to 10 + 1 milliseconds, in order to ensure that the first button push action is not inadvertently ignored as bounce.
Main-loop driven part
## InputGetSelectorPushed()
## This function is called from the main loop, and its output is stored into the system-state memory. If implemented via interrupt, the reading routine should disable the selector interrupt while reading and clearing the value.
Return Values R	Action
R == 0	Selector has not been pushed
R != 0	Selector has been pushed
Table 2. Return values of GetSelectorPushed()
## Shift enable toggle switch
## When the shift enable switch is activated, the repeater shift Values is added to the VFO frequency when switching to transmit mode.
## Once every iteration of the main loop, the signal is checked and its result stored in the system-state memory.
## InputGetShiftEnable()
Return Values R	Action
R == 0	Repeater shift disabled
R != 0	Repeater shift enabled
## Table 3. Return values of GetShiftEnable()
## Tx/Rx toggle switch
## When the Tx/Rx switch is activated, system switches to transmit mode.
Once every iteration of the main loop, the signal is checked and its result stored in the system-state memory.
## InputGetPTT()
Reads the input Values from the IO register.
Return Values R	Action
R == 0	PTT idle
R != 0	PTT is on
## Table 4. Return values of GetPTT()
## S-Meter ADC
## InputGetSMeter()
## Reads the numerical Values of the current signal strength as is measured by the ADC from the IF output signal.
  1. Output functions
In general, once every iteration of the main system loop, the current setting of the outputs are compared to potential new values If a change is detected the new Values is written out to the hardware. The new Values is obviously also copied to a variable holding the current state of the hardware.
    1. PLL Synthesizer controls
## OutputSetVFO(long int divider);
    1. PLL reference control
## OutputSetPLLReference(long int reference);
    1. Display controls
Several functions described below actually make up the display control. Each of the values.
    1. CTCSS signal
The CTCSS signal is a square wave between roughly 60 and 160 Hz, that is generated by the CPU . Implementation is either via a timer interrupt followed by a toggle instruction, or via a free running timer that inverts its output and reloads on every timeout.
    1. Audio mute switch
Simple line that mutes audio. When the signal is programmed hight, audio is muted. Once every iteration of the main system loop, the Values of the system-state variable mute is copied into the mute output bit.
    1. Frequency on display
    2. S-Meter on display (discrete)
Once every iteration of the main system loop, it is checked whether to S-meter Values from the ADC differs from the one store in system-state memory. If so, the new Values is written out the the display and the system-state Values is updated.
    1. Tx/Rx indicator on display
Once every iteration of the main system loop, the Values of the system state variable Transmitting is compared to its previous value. If a change occurred, the new Values will be used to change the 'T'/'R' indicator on the display.
    1. Mute indicator on display
Once every iteration of the main system loop, it is checked whether the mute state has changed since the last iteration. If so, the 'M/' ' Values on the display is updated.
  1. System-state memory
The system-state memory is filled in the main loop by calling the input routines. In the second half of the loop (the output part) the hardware is made to conform to the content of the system-state memory. In general the state of the hardware will be preserver in separated values. For every piece of hardware it will be checked if the system-state Values differs from the current value. Only when there is a difference will the hardware settings be changed, thus preventing expensive (read: time consuming) actions that are not necessary, and that degrade the responsiveness of the system.
    1. Input related memory
Internal Rotary dial, up/down action
Reflects what the user has done with the rotary dial since the last read-out.
This value is updated by an interrupt service routine and should only be retrieved with the accompanying function: InputGetRotaryDialCount()
Name	IRQ_RotaryCount
Type	integer
Values	min_int … max-int
Public Rotary dial, up/down action
Reflects what the user has done with the rotary dial since the last read-out.
This value is stored in the system state memory by a call to InputGetRotaryDialCount() from the main loop.
Name	SS_RotaryCount
Type	integer
Values	min_int … max-int
Internal Selector switch
This value is stored in the system state memory by a call to InputGetSelector() from the main loop.
Name	IRQ_SelectorPushed
Type	char
Values	{ 0, ~0 } 0 = idle, ~0 = selector switch pushed
Public Selector switch
This value is stored in the system state memory by a call to InputGetSelector() from the main loop.
Name	SS_SelectorPushed
Type	char
Values	{ 0, ~0 } 0 = idle, ~0 = selector switch pushed
Repeater shift enable
This is a toggle switch on the front-panel. Its position is sampled with every iteration of the main loop. The resulting value is stored in the system state memory
Name	SS_ShiftEnable
Type	char
Values	{ 0, ~0 } 0 = normal, ~0 = repeatier shift active during transmit
Tr/Rx (ptt)
This is a toggle switch on the front-panel and/or on the microphone. Its position is sampled with every iteration of the main loop. The resulting value is stored in the system state memory
Name	SS_PTT
Type	char
Values	{ 0, ~0 } 0 = receive mode, ~0 = transmit mode
    1. Internal memory values
Menu position
Menu position is the variable that keeps track of the position in the menu structure that the state-full menu-system is currently residing.
Name	SS_MenuState
Type	integer
Values	lower 16 bits are ….. upper 16 bits are...
Direct menu return
Direct menu return allows the user to choose between returning immediately back to receive mode after choosing and/or changing a value, or closing the edit mode and return to the menu-system in order to make a next selection.
Name	SS_DirectMenuReturn
Type	char
Values	{ 0 , ~0 } 0 = up 1 level, ~0 = return to receive mode
CTCSS tone index
The CTSCSS tone index Values contains an index in to the array of frequency values that should be injected in the modulation during transmit.
Name	SS_CtcssIndex
Type	integer
Values	0 = no output
other valid values are: { }
S-meter mute value
S-meter mute Values holds the threshold below which the audio is muted.
Name	SS_MuteLevel
Type	integer
Values	0 … 64
Base frequency
Base frequency holds the frequency Values the system is currently operating at. Other frequency values are derived from the base frequency value
Name	SS_BaseFrequency
Type	long integer (32 bit)
Values	1260000 … 1300000
Base-frequency will in most cases reflect the frequency that the system is listing on in receive mode.
Operating Mode	Display Frequency	VFO / Frequency
Receiving	BF	BF - IF
Transmitting	BF	BF
Receive with repeater shift	BF	BF - IF
Transmit with repeater shift	BF + SHIFT	BF + SHIFT
Receive with repeater shift reversed	BF + SHIFT	BF + SHIFT - IF
Transmit with repeater shift reversed	BF	BF

Table , How different frequencies are derived from the BaseFrequency (BF)
VFO tx/rx shift value
VFO tx/rx shift Values holds the frequency amount the VFP shifts downwards for repeater shift during transmit.
Name	SS_FrequencyShift
Type	long integer (32 bit)
Values	-60000 … 60000
Transmitting
Determines whether the system should be in transmit mode or receive mode.
Name	SS_Transmitting
Type	char
Value	{ 0 , ~0 } 0 = Receive, ~0 = Transmit
Muted
Determines whether the system mutes the audio output.
Name	SS_Muted
Type	char
Values	{ 0 , ~0 } 0 = audio on, ~0 = audio muted
Shift Enable
Determines whether the VFO will apply repeater shift during transmit.
Name	SS_ShiftEnable
Type	char
Values	{ 0 , ~0 } 0 = no shift, ~0 = shifted
Reversed
Determines whether the system does a reverse shift on transmit and receive frequencies. This is a convenient way to quickly listen on repeater input channels.
Currently there is no input control available to allow for reverse shift. Via remote control however the usage of this function is perfectly feasible
When this variable is set, the repeater shift Values will be added to the VFO frequency during receive mode instead of during transmit.
Name	SS_Reversed
Type	char
Values	{ 0 , ~0 } 0 = normal, ~0 = reversed.
    1. Output related memory
Display frequency
The frequency Values that will be shown on the display
Name	SS_DisplayFrequency
Type	long integer (32 bit)
Values	1260000 … 1300000 (band bottom … band top)
See table under BaseFrequency for the way this Values is calculated from the base-frequency.
Display S-meter
The level that will be indicated by the S-meter bar on the display.
Name	SS_DispSMeter
Type	integer
Values	0 … 64
Display menu
t.b.d.
Current VFO frequency
Frequency Values that the PLL must generate according to the current base-frequency and operating mode. See the table under BaseFrequency for the way this Values is calculated.
On output this Values is used to calculate the divider Values programmed into the PLL divider chain.
Name	SS_VFOFrequency
Type	long inteer (32 bits)
Values	0 … max-int
PLL Reference frequency
Values to be programmed into the PLL divider chain for the reference frequency. The original design has a 12 MHz discrete component crystal oscillator. Using a 13 MHz TCXO with higher frequency stability is a popular modification.
Name	SS_PLLReferenceFrequency
Type	long integer (32 bits)
Values	0 … max-int
Display Mute Indicator
Values that will be written to the mute_audio output.
Name	SS_MuteIndicator
Type	char
Values	boolean { 'M”, ' ' }
Muted
Values that will be written to the mute_audio output.
Name	SS_Muted
Type	char
Values	boolean { 0, ~0 } 0 = not muted. ~0 = muted
Transmitting
Value that will be written to the transmitter_on output.
Name	SS_Transmitting
Type	char
Values	boolean { 0, ~0 } 0 = Rx, ~0 = Tx
Display TxRx indicator
Writes a T or R tot the display.
Name	SS_TxRxIndicator
Type	char
Values	boolean { 'R' , 'T' }
CTCSS output
The frequency that will be injected during transmit
Name	SS_CTCSSFrequency
Type	int
Values	ing { 600, 2000 } in 1/10 of a Herz, so 885 is 88.5 Hz
  1. Initialization
As part of the system power-on sequence, several values in the system-state memory need to be initialized to a predefined value. With some exceptions, the predefined values are retrieved from non-volatile memory. Here they are part of the remembered state from the moment the system was switched off, or they are part of the configured values that go with specific hardware variations.
  1. Menu-system
- off : rotary-dial selects frequency
- Select button pushed:
  - Mute-level
  - CTCSS frequency
  - Scan
  - Repeater shift amount
  - Scan start frequency
  - Scan stop frequency
  - Configuration:
    - PLL reference frequency (MHz)
    - PLL reference frequency (kHz)
    - PLL reference frequency (Hz)
    - Remote control baud-rate
    - Direct menu return
    - Disable remote-control
    - Re-enable front panel controls
    - Reset to factory defaults
    1. Mute-level
    2. CTCSS frequency
    3. Scan
    4. Repeater shift amount
    5. Scan start frequency
    6. Scan stop frequency
  2. Configuration
This is a sub-menu that allows detailed settings of the tranceiver to be managed.
    1. SMeterCalibration
Default value = 1.00
Minumum = 0.50, Maximum = 2.00
Used to calibrate the exact number of lines in the display per μV input signal.
    1. PLL reference frequency (MHz)
Default value = 13 MHz
    1. PLL reference frequency (kHz)
Default value = 0 kHz
    1. Remote control baud-rate
Default value = 9600 baud
    1. Direct menu return
When set: activating the select push button causes an immediate return to tuning mode, instead of 1 level up in the menu system.
    1. Disable remote-control
When set: the input from the remote control station is ignored.
    1. Re-enable front panel controls
The remote control can disable front-panel controls. This is a conveniance feature, and not a security measure. With this submenu item, full control can be restored to the front-panel.
    1. Reset to factory defaults
In order to offer a way to load a guaranteed set of values into the system, the reload factory default function is provided.
The non-volatile memory is wiped, and a new set of values is written.
- BaseFrequency	1298.200 MHz.
- RepeaterShift	-28 MHz
- PLL reference frequency	12.000 MHz
- Remote control UART	9600 baud, 8 bit, no parity, 1 stop bit
- Direct menu return	Off
- Transmitting	False
- Shifted	False
- ReverseShift	False
- Muted	False
- MuteLevel	0
- SmeterCalibration	1
- CtcssIndex	0
- Scanning	False
- ScanStartFrequency	Band Bottom	(1.240 GHz)
- ScanEndFrequency	Band Top	(1.300 GHz)
- Enable Remote Control	True
- Disable Front Panel	False